## Slide 1
Water Management of the Okanagan Lake Regulation System
October 2015
Presented to the Osoyoos Lake Water Science Forum
Shaun Reimer, P.Eng.
Public Safety & Protection
Ministry of Forest, Lands and
Natural Resource Operations
Penticton

## Slide 2
Tributary to Columbia River
Okanagan Basin Drainage area = 8,200 km2 (in Canada)
Main stem lakes:
  Kalamalka/Wood (3520 ha; 8700 acre)
  Okanagan (34075 ha; 84200 acre)
  Skaha (2023 ha; 5000 acre)
  Vaseux (243 ha; 600 acre)
  Osoyoos (2318 ha; 5728 acre)
Watershed Description

## Slide 3: Skaha Lake Dam
Similkameen R.
Okanagan R.
Columbia R.
Okanogan R.
Columbia R.
Osoyoos Lake
Okanagan Lake Dam
Kalamalka Lake Dam
McIntyre Dam

## Slide 4
System extends from Kalamalka Lake to north end of Osoyoos Lake
4 dams (Kalamalka, Okanagan, Skaha & Vaseux Lakes)
17 vertical drop structures
38 km of engineered channel, including 68 km of dikes
4 sediment basins
Okanagan Lake Regulation System

## Slide 5
Okanagan Lake Dam
Skaha Lake Dam
Vaseux (McIntyre) Dam
Photo courtesy of ONA
VDS 10
OLRS Structures

## Slide 6
Construction of the Okanagan Flood Control System
A Joint Board of Engineers:
  Appointed in 1943 to report out after a major 1942 flood;
  Recommended the construction of dams, vertical drop structures, and river channelization, as well as the establishment of operating ranges;
Recommendations were implemented after a “Memorandum of Agreement” was signed in 1950 between the Federal and Provincial governments;
Project was completed between 1950 &1958;
Costs of the construction and maintenance were shared equally.

## Slide 8
Okanagan River in 1938 and in 1996

## Slide 9
Okanagan Basin Implementation Agreement
In 1976, the Okanagan Basin Implementation Agreement was signed by the Federal and Provincial Governments;
It set out seasonal targets for main stem lake elevations and river flows. These targets take into account:
  Anticipated flood and prolonged drought conditions;
  Water requirements for Sockeye and Kokanee
Some infrastructure was upgrades and repaired (1976-1981);
Under this agreement, the Province became the operators of the Okanagan Flood Control System.

## Slide 10
Okanagan Lake operational range: 1.15 m
  341.34 m to 342.48 m geodetic;
  Under prolonged drought conditions (successive years <247 Million m3), lake may be drawn down to 340.4 m;
Average inflow into Okanagan Lake: 530 Million m3 (1.5 m on lake);
How are decisions made??
Range of Flows and Lake Levels

## Slide 11
Computer Model used for decision making support;
Forecasts Okanagan Lake and River levels based on inflow forecasts from River Forecast Centre (Victoria) and a Release Schedule from Okanagan Lake Dam;
Uses peak spawning dates and temperature data to inform the water manager of fish hatching and emergence;
Seasonal or monthly target levels conform to those developed under the Okanagan Basin Implementation Agreement.
Partners include Douglas County PUD (US), DFO, ONA, FLNRO.
Fish Water Management Tool

## Slide 12
Mission Creek
SWE - 12th April
Brenda Mine
Grano Creek
Blackwall Peak
Monitoring Snow

## Slide 13
Management Tool
Decision Makers (Multidisciplinary team)
Satellite
Snow pack
Runoff
Lake level
Discharge
Temp / O2
Okanagan Lake
Okanagan River
Osoyoos Lake
Dam
Fisheries

## Slide 14
February 2015
Fish Water Management Tool Output

## Slide 15
Chart: Weekly Net Inflows - Okanagan Lake (mil. m3)
| Jan-07 | Jan-14 | Jan-21 | Jan-28 | Feb-04 | Feb-11 | Feb-18 | Feb-25 | Mar-04 | Mar-11 | Mar-18 | Mar-25 | Apr-01 | Apr-08 | Apr-15 | Apr-22 | Apr-29 | May-06 | May-13 | May-20 | May-27 | Jun-03 | Jun-10 | Jun-17 | Jun-24 | Jul-01 | Jul-08 | Jul-15 | Jul-22 | Jul-29 | Aug-05 | Aug-12 | Aug-19 | Aug-26 | Sep-02 | Sep-09 | Sep-16 | Sep-23 | Sep-30 | Oct-07 | Oct-14 | Oct-21 | Oct-28 | Nov-04 | Nov-11 | Nov-18 | Nov-25 | Dec-02 | Dec-09 | Dec-16 | Dec-23 | Dec-31
Average | 2.2767 | 3.0744 | 4.0256 | 3.2047 | 3.3767 | 3.9581 | 4.4372 | 4.7977 | 5.1884 | 5.3372 | 7.1 | 7.2465 | 7.9581 | 11.0372 | 14.3419 | 21.2907 | 32.5279 | 40.7814 | 46.0465 | 54.4302 | 56.8209 | 49.6721 | 40.1535 | 33.1721 | 24.3279 | 16.5953 | 11.0698 | 6.507 | 3.2395 | 0.90233 | -2.0558 | 1.9372 | -5.8744 | -3.2116 | -1.7233 | -2.0907 | -1.4326 | -0.73721 | -1.3744 | -1.6857 | -1.3071 | 0.68333 | 1.3667 | 1.5976 | 1.75 | 2.6619 | 1.9143 | 2.5381 | 1.2429 | 2.5452 | 2.0905 | 2.8643
Current | 13.4 | 3.4 | 7.8 | 5 | 11.5 | 19.3 | 19.3 | 10.7 | 6.6 | 8.7 | 19.3 | 31.9 | 22.4 | 42.7 | 18.6 | 25.1 | 26.4 | 25.1 | 24.3 | 35.7 | 28.4 | 34.1 | 16.9 | 3.5 | 0.4 | 0.8 | -5.7 | -8.1 | -10.2 | -4.1 | -5.5 | -1.1 | -6.9 | -11.2 | -6.7 | -4.8 | -5.3 | -5.7 | -3.5
Fish Water Management Tool Output

## Slide 16
Management Constraints
Okanagan River Design Flows range from 60 m3/s in Penticton to 96 m3/s south of Oliver;
Net difference of 40 m3/s (inflow - outflow) on Okanagan Lake = 1 cm/day.
Seasonal constraints include maximum flow of 28.3 m3/s (1000 cfs) in Okanagan River at Oliver until Sockeye eggs hatch and emerge from gravel;
  This constraint overridden for large snowpacks;
  Tributary flow downstream of Penticton means that this flow may be much less out of Okanagan Lake Dam.

## Slide 18
Similkameen River Impacts
Similkameen River enters Okanogan River below Zosel Dam;
High Similkameen flow (> 10000 cfs) slows the Okanogan River (backwaters) or even reverses flow northward and potentially increases Osoyoos Lake levels;
Okanagan River releases at Okanagan Lake Dam have been reduced in the past to reduce the impact of high peaks on the Similkameen.

## Slide 19
This Year: 2015
Warm winter and early snowmelt meant that Lake was higher than target values for much of spring;
2015 Peak Net inflow to Okanagan Lake approximately 460 Million m3 (1.33m);
Dry summer with warm lake temperatures adding to high evaporation;
15 centimetres lower than September target elevations (beginning and end).
Chart: Okanagan Lake - 2015
| 41919 | 41926 | 41933 | 41940 | 41947 | 41954 | 41961 | 41968 | 41975 | 41982 | 41989 | 41996 | 42004 | 42011 | 42018 | 42025 | 42032 | 42039 | 42046 | 42053 | 42060 | 42067 | 42074 | 42081 | 42088 | 42095 | 42102 | 42109 | 42116 | 42123 | 42130 | 42137 | 42144 | 42151 | 42158 | 42165 | 42172 | 42179 | 42186 | 42193 | 42200 | 42207 | 42214 | 42221 | 42228 | 42235 | 42242 | 42249 | 42256 | 42263 | 42270 | 42277
Forecast | 341.7529
Actual | 341.9361 | 341.9109 | 341.8894 | 341.8761 | 341.8577 | 341.8457 | 341.8127 | 341.7984 | 341.8171 | 341.8032 | 341.8129 | 341.8183 | 341.825 | 341.8276 | 341.8465 | 341.8479 | 341.847 | 341.8463 | 341.8648 | 341.891 | 341.8999 | 341.8897 | 341.8758 | 341.8857 | 341.9277 | 342.0016 | 342.0702 | 342.1147 | 342.1443 | 342.1966 | 342.2406 | 342.2695 | 342.3046 | 342.3389 | 342.3524 | 342.3789 | 342.3324 | 342.2822 | 342.2463 | 342.2071 | 342.1631 | 342.1108 | 342.0694 | 342.0365 | 342.0026 | 341.9756 | 341.9266 | 341.8852 | 341.8437 | 341.8218 | 341.7851 | 341.7585


 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4 | 345.4


 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345 | 345


 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6 | 344.6
 | 344.2 | 344.2 | 344.2 | 344.2

## Slide 20
Mission Creek Automated Snow Pillow

## Slide 21
Questions?